## Slide 1: Soft X-Ray Spectrometers for Absorption Spectroscopy of Aluminum in Laser Driven Backlighter Experiments
Master’s Thesis Presentation by Carlos Butler
Department of Plasma Physics/PHELIX at GSI

## Slide 2
Motivation
Spectrometer Design
Experiment
Outlook
Results and Discussion

## Slide 3: Warm Dense Matter (WDM)
State between condensed matter and weakly coupled plasma
Relevant for:
  Astrophysics
  Inertial confinement fusion
Experimental challenges:
  Producing extreme conditions in a controlled way
  Short lifetimes (
  Opaque in optical range
Riley D., Plasma Phys. Control. Fusion 60, 2018
Notes: WDM at or above solid density
One by one

## Slide 4: Warm Dense Matter (WDM)
State between condensed matter and weakly coupled plasma
Relevant for:
  Astrophysics
  Inertial confinement fusion
Experimental challenges:
  Producing extreme conditions in a controlled way
  Short lifetimes (
  Opaque in optical range
Riley D., Plasma Phys. Control. Fusion 60, 2018
Dump energy in short time and small volume
X-rays for diagnostics

## Slide 5: Experimental Scheme
Unique pump-probe scheme at FAIR:
  Heavy-ion beam for WDM generation
  Laser-plasma as x-ray source
Homogeneous WDM sample with fast, tunable x-ray source
Heavy-ion
Beam
Sample
Backlighter
Target
Intense Laser
Diagnostic?  X-ray Absorption Fine-structure Spectroscopy (XAFS)
Measuring
Device
Measuring
Device
WDM
Plasma
Transmitted
X-rays
Reference
X-rays

## Slide 6: X-Ray Absorption Fine-Structure (XAFS)
Studies structures around edge (rapid rise) in absorption spectrum
X-rays
Transmitted
Transmitted x-rays
Spectrometers
Source
For WDM, can extract:
  Density
  Temperature
  Ionic order
  Ionization
Photon Energy
Absorption Coefficient
Al Sample
Source
Notes: A mature method used in numerous fields (biology, solid-state physics, since 1988 WDM research
Edge is jump in absorption at ionization energy of a shell

## Slide 7: XAFS Example for Aluminum
X-ray Absorption Near Edge Structure (XANES)
Extended X-ray Absorption Fine-Structure (EXAFS)
For example:
Amplitude of oscillations  temperature
Resolution requirements:
XANES: eV
EXAFS: 0 eV
High T Low T
Photon Energy [eV]
Absorption Coefficient []
1560
1700
1600
0.1
2

## Slide 8: Overview
Overarching project: Probe WDM of aluminum with x-rays from laser-plasma backlighters using XAFS
Requirement: Specialized spectrometers
Sample
Intense Laser
Heavy-ion
Beam
Backlighter
Target
Measuring
Device
Measuring
Device
PHELIX
Aluminium
Sample
X-ray Spectrometer
X-ray Spectrometer
Thesis goal: Design and test x-ray spectrometers

## Slide 9: Fundamentals of X-Ray Spectrometers
Purpose: Measure intensity of photons depending on energy
Main parameters:
  Spectral resolution
  Energy range
  Efficiency
Main design decisions:
  Crystal material and form
  Geometry
Challenges:
  Limited crystal choice
  XANES: 1540 – 1620 eV with eV
  EXAFS: 1540 – 1800 eV with eV
Approach: Test two schemes
  Flat crystal  simple and reliable
  Bent crystal  more complex but higher potential
Crystal
X-ray Source
Detector
Notes: Focus on challenges of setup and creating the spectrometer due to restrictions, rather than design philosphies
Spectral resolution: the lower the better

## Slide 10: Flat-crystal Spectrometer
View on Detector
Ion beam
(Future Experiment)
ADP Crystal
ADP Crystal
Detector
Backlighter
Target
Sample
Top view:
Side view:
ADP Crystal
Detector
Backlighter
Target
Sample
Dual Unbent Crystal speCtrometer (DUCC)
Laser Beam
Laser Beam
From simulation:
Energy range of 1540 – 1620 eV
Resolution of 0.7 eV
Suited to XANES!

## Slide 11: Bent-crystal Spectrometer
Spherically-bent crystal  works similarly to a convex mirror
Spectral focusing in dispersive plane
1-D imaging in vertical plane
Mica crystal
Rowland Circle
Detector
Source
Vertical
Dispersive
Dispersive
Source
On detector
Vertical
Focusing Spectrograph with Spatial Resolution in 1-D (FSSR-1D)
From simulation:
Energy range of 1465 – 1755 eV
Resolution of 0.56 eV
Suited to EXAFS!

## Slide 12: Comparison
DUCC
FSSR
Flat crystal  simple, robust geometry
ADP crystal  good crystal properties
Dual channel  absorption spectra with one spectrometer
Spherically-bent crystal  high intensity and resolution
Mica crystal  common in literature
1-D imaging  good signal-to-noise ratio
Spectrometer | Regime | Energy Range | Resolution
DUCC | XANES | 1540 – 1620 eV | 0.7 eV
FSSR | EXAFS | 1465 – 1755 eV | 0.56 eV

## Slide 13: Fabrication
  DUCC: Flat crystal design
  FSSR: Bent crystal design

## Slide 14: Experimental Setup
KAP Crystal
Backlighter
PHELIX
Al Sample
DUCC Spectrometer
X-Ray
Camera
SUCC
Spectrometer
X-Ray
Camera
FSSR-1D
Spectrometer
X-Ray
Camera
Two additional spectrometers by P. Hesselbach: Single Unbent Crystal speCtrometer (SUCC) and Old SUCC (OSUCC)
  Flat-crystal geometry with KAP crystal
  Energy range of 1400 – 1800 eV
  SUCC for control spectra
  OSUCC for transmitted spectra (can replace FSSR)
Three backlighter materials:
  Rare-earths: Intense emission but with structure
  Teflon: Weaker emission but smooth spectrum
  Aluminum: For spectrometer characterization
Goal: Find spectrometer + backlighter combination that yields smooth, high resolution absorption spectra

## Slide 15: Data Processing
Use self-developed python program: Analysis of X-ray Absorption for WDM Observation and Testing of Locally-made Spectrometers (AXAWOTLS)
  Quick processing of raw images to spectra and analysis during beamtimes
  Adaptable to any spectrometer
Study two sets of results:
Result | Type | Criteria | Influenced by
Spectral resolution | Quantitative | For EXAFS eV For XANES eV | Geometry, crystal quality
Absorption spectra | Qualitative | Smoothness, agrees with literature | Backlighter, crystal quality, spectrometer pairing
Result | Type | Criteria | Influenced by
Spectral resolution | Quantitative |  | Geometry, crystal quality
Absorption spectra | Qualitative | Smoothness, agrees with literature | Backlighter, crystal quality, spectrometer pairing

## Slide 16: Spectral Resolution
Gaussian Fit of the He-α emission line of aluminum backlighter
Deconvolve FWHM and Doppler broadening  spectral resolution

## Slide 17: Spectral Resolution
Gaussian Fit of the He-α emission line of aluminum backlighter
Deconvolve FWHM and Doppler broadening  spectral resolution
DUCC’s resolution insufficient for XANES
FSSR and SUCC sufficient for EXAFS
Main Contribution: Crystal broadening  Crystal quality is limiting factor
Spectrometer | Required | Simulated | Experimentally Determined | Crystal Broadening
DUCC | eV | 0.70 eV | eV | eV
FSSR | eV | 0.56 eV | eV | eV
SUCC | - | - | eV | eV
Spectrometer | Required | Simulated | Experimentally Determined | Crystal Broadening
DUCC |  | 0.70 eV |  | 
FSSR |  | 0.56 eV |  | 
SUCC | - | - |  | 

## Slide 18: Absorption Spectra
Use transmitted and source spectra for absorption coefficient
is material property dependent on photon energy
DUCC produces alone, otherwise spectrometer pairing
Compare best backlighter material + spectrometer pairings
Trans-mitted
Source

## Slide 19: Absorption Spectra
Spectrometers | Backlighter | Quality
DUCC | Rare-earth | 
OSUCC/SUCC | Teflon | 
FSSR/SUCC | Teflon | 
DUCC
DUCC
Notes: Explain why the combinations are chosen in more detail

## Slide 20: Absorption Spectra
Spectrometers | Backlighter | Quality
DUCC | Rare-earth | 
OSUCC/SUCC | Teflon | 
FSSR/SUCC | Teflon | 
OSUCC
SUCC

## Slide 21: Absorption Spectra
Spectrometers | Backlighter | Quality
DUCC | Rare-earth | 
OSUCC/SUCC | Teflon | 
FSSR/SUCC | Teflon | 
FSSR
SUCC
X

## Slide 22: Summary
Thesis goal: Design and test x-ray spectrometers for XAFS of aluminum to use in WDM research with heavy-ion beam sample heating and laser-plasma backlighters
Tested two schemes:
  Flat crystal  DUCC with ADP crystal (simple, dual channel)
  Bent crystal  FSSR with mica crystal (complex, focusing)
Additionally in experiment: SUCC and OSUCC with KAP crystal
Results:
DUCC:
  + Dual channel design effective for absorption spectra
  ­­– Insufficient resolution (1.68 eV > 1 eV)
FSSR:
  + High resolution (1.72 eV << 10 eV)
  ­­– Absorption edge in mica crystal  poor absorption spectra
SUCC:
  + Good resolution (2.84 eV << 10 eV)
  ­­+ Excellent absorption spectra with OSUCC/SUCC

## Slide 23: Outlook
  Crystal quality significant to resolution  characterize crystals before finalizing design!
  DUCC has potential if crystal quality ensured
  FSSR is powerful, but adds complexity and requires a different crystal
  From SUCC, design with flat KAP crystal and Teflon backlighter effective for EXAFS
  Dual channel layout leads to high quality absorption spectra
DUCC and FSSR have potential for future experiments!
Next spectrometer: Dual channel geometry with KAP crystals and Teflon backlighter!
High quality EXAFS in heavy-ion beam + PHELIX laser experiment of 2024

## Slide 24
Thanks for your attention!
Next spectrometer: Dual channel geometry with KAP crystals and Teflon backlighter!
High quality EXAFS in heavy-ion beam + PHELIX laser experiment of 2024

## Slide 25: X-Ray Absorption Fine-Structure (XAFS)
Studies structures around edge (rapid rise) in absorption spectrum
Structures caused by quantum scattering
X-rays
Sample
Transmitted x-rays
Spectrometer
Source
X-ray
Atoms in lattice
Photoelectron wavefunction
Back-scattered wavefunction
For WDM, can extract:
  Density
  Temperature
  Ionic order
  Ionization
Notes: A mature method used in numerous fields (biology, solid-state physics, since 1988 WDM research
Edge is jump in absorption at ionization energy of a shell
Process in diagram happens in sample (point out)
XAFS: 1) x-ray photoionizes electron from absorbing atom
2) photoelectron quantum mechanically scatters on neighboring electron
3) part of wavefunction reflected back to absorbing atom
4) Backscattered wavefunction modulates electronic state at first atom
5) absorption coefficient dependent on electronic state  modulates mu as well  structures dependent on lattice and structure
IMPORTANT: all happens in a single coherent quantum state at absorbing atom  all absorption events effected!
Next will see example of an absorption spectrum

## Slide 26: Considerations
Energy Range
Sample Size
Resolution
Intensity
Physical Size
X-Ray Absorption Fine-Structure: Al K-edge at 1560 eV
Near edge (XANES): 1540 – 1620 eV
Extended (EXAFS): up to 1800 eV
homogeneous heavy-ion beam heating of sample  small sample  small range projection on sample (<1 mm)
Enough to resolve XAFS 
XANES: 1 eV
EXAFS: 10 eV
High as possible without saturation
Fit in HHT chamber  length < 550 mm

## Slide 27
Consideration | Limit | DUCC | FSSR
Energy range | XANES: 1540-1620 eV EXAFS: up to 1800 eV | 1541-1618 eV (XANES) | 1465-1755 eV (XANES+EXAFS)
Sample Size | < 1 mm | 0.51 mm | 0.76 mm
Spectrometer length | < 550 mm | 235.2 mm | 404.3 mm
Resolution | XANES: 1 eV EXAFS: < 10 eV | 0.70 eV | 0.56 eV
Consideration | Limit | DUCC | FSSR
Energy range |  | 1541-1618 eV (XANES) | 1465-1755 eV (XANES+EXAFS)
Sample Size | < 1 mm | 0.51 mm | 0.76 mm
Spectrometer length | < 550 mm | 235.2 mm | 404.3 mm
Resolution |  | 0.70 eV | 0.56 eV

## Slide 28
Take line outs of each section
Flip spectra if needed, correct background, and convert pixel number to photon energy
Correct out filters, camera effects, and geometry, then bin the data
Spectrum 1
Background
Spectrum 2
Dispersion

## Slide 29: Components and Requirements
Main Components | Purpose
Greateyes x-ray camera | Record spectra
Aluminum housing | Structure and shielding
Carbon filters | Insulation of camera chip
Mylar (plastic) filters | Shielding of crystals
Alignment apparatus | Alignment
Requirements:
Implementation of design ( mm precision)
Shielding of sensitive elements
Alignment in chamber
Robustness

## Slide 30: DUCC
Top
Scheme
Front/Side
Front
Back
Camera
Tilt
Blast Shields
Pointer Holder
Carbon Filter Holder

## Slide 31: FSSR
Scheme
Top
Front
Back
Inside Snout
Blast Shield
Crystal
Main Shielding
Snout
Stages for Alignment
Carbon Filter Holder

## Slide 32: Sample Size Consideration
Crystal
Source
Sample
Ion beam
(Future Experiment)

